PSU Clamp Test Waveforms & Calculations
April & May 2025

# Setup
Motor: EMAX ECO 1106, Kv = 6000, 12 magnets, with flywheel
Connections: Separate connection from power supply to Remora & from power supply to the clamp circuit
Clamp Circuit Schematic	Q1: the prototype used SQJ140ELP mounted on a copper sheet 15mm × 8mm × 0.5mm / A few other possible mosfet candidates: / Part Number Package / SQJ140ELP PowerPAK (5x6) / SQJ160EP PowerPAK (5x6) / IRFS7437 D²PAK / SQM40016EM D²PAK 7 lead / RFP50N06 TO-220 / SUP50020EL TO-220 / IRLB3034 TO-220 / Q2: the prototype used KSA733, but almost any small PNP transistor would work.

# Method
In the ESC32 menu move slider right then left, this rapidly stops the motor sending energy back to the power supply (PSU), as power supplies only source current this raises the PSU voltage.
The clamp is designed to start operating at about 12.5V preventing damage to the WiFi and Remora.

ERPM = rpm × pole pairs ∴ rpm = ERPM ÷ pole pairs ∴ rpm = 186335 ÷ 6 = 31056rpm
From Kv value: rpm ≈ 5V × 6000Kv = 30000rpm, so in reasonable agreement with ERPM reading from ESC32.
Commutation frequency, Fc = (rpm / 60) × pole pairs = ERPM / 60 = 186335/60 = 3106Hz
Measured Fc from oscilloscope is 3003Hz
Supply rail voltages & mosfet gate voltage
	1 / 5V supply / green = supply at Remora, 5V/div, 10ms/div / Supply starts at 5V, then when the slider is moved left it rapidly rises to the clamp level of about 12.5V. / The clamp successfully holds the voltage at below 15V.
	2 / 5V supply / yellow = mosfet gate, 1V/div, 500µs/div / green = supply at clamp, 5V/div, 500µs/div / The pulses occur at 3× the commutation frequency. / Initially at ≈115µs period ≈ 9kHz / Therefore one pulse for each of the ecom 3 phases. / See waveform 4 for an individual phase.
	3, zoom of 2 / 5V supply / yellow = mosfet gate, 1V/div, 10µs/div / green = supply at clamp, 5V/div, 10µs/div / Gate voltage returning to zero indicates that the mosfet is being turned on & off during the clamping phase. / The voltage remaining high must then be due to the capacitance in the PSU & Remora.
	4 / 5V supply / yellow = ecom V phase output, 5V/div, 500µs/div / green = supply at Remora, 5V/div, 500µs/div / The high amplitude (>10V) spikes on V-phase occur at the commutation frequency.
currents / (Remora settings slightly different to those for voltage measurements above, running at slightly higher rpm)
	5 / 5V supply / yellow = supply at Remora, 5V/div, 500µs/div / green = current in Remora +ve line, 2A/div, 500µs/div / The spikes occur at 3× the commutation frequency, i.e. one for each phase. / Initially at ~ 110µs period
	6 zoom of 5 / 5V supply / yellow = supply at Remora, 5V/div, 5µs/div / green = current in Remora +ve line, 2A/div, 5µs/div / 6A peak current fed from Remora to PSU & clamp circuit. / Approximately a triangular shape width 20µs / So average current ≈ 6A ÷2 × 40µs ÷ 110µs = 1.1A / The current & voltage both start to rise at the same time, but peak current is lags the peak PSU voltage by about 6.8µs
	7 / 5V supply / yellow = supply at Remora, 5V/div, 500µs/div / green = current in clamp +ve line, 2A/div, 500µs/div
	8 zoom of 7 / 5V supply / yellow = supply at Remora, 5V/div, 10µs/div / green = current in clamp +ve line, 2A/div, 10µs/div / peak current & width are very similar to the current from Remora, but some current must be flowing into the power supply output capacitor as indicated by the rise in the voltage. / The rise in current is delayed from the start of the voltage rise & the peak current lags the peak PSU voltage by about 9µs
	9 / 5V supply / yellow = supply at Remora, 5V/div, 500µs/div / green = current in PSU +ve line, 2A/div, 500µs/div
	10 zoom of 9 / 5V supply / yellow = supply at Remora, 5V/div, 5µs/div / green = current in PSU +ve line, 2A/div, 5µs/div / The current & voltage both start to rise at the same time, and peak current is coincident with the peak PSU voltage
	11 / 11.5V supply / yellow = supply at Remora, 5V/div, 10ms/div / green = current in clamp +ve line, 5A/div, 10ms/div
	12, as 11 but faster time-base / 11.5V supply / yellow = supply at Remora, 5V/div, 500µs/div / green = current in clamp +ve line, 5A/div, 500µs/div
	13 zoom of 12 / 11.5V supply / yellow = supply at Remora, 5V/div, 10µs/div / green = current in clamp +ve line, 5A/div, 10µs/div / ipk = 14.5A / iav from scope measurement =4.22A / irms from scope measurement = 6.1A / current prior to steep rise = 2.3A / period = 49.4µs / Approximately a triangular shape width = 23µs / 2.3A step width = 9.4µs / 0A to 2.3A ramp width = 10µs / check on iav: / Iav ≈ [(14.5÷2×23µs)+ (2.3÷2×10µs) + (2.3×9.4µs)]÷ 49.4µs = 4A, in reasonable agreement with scope measurement. / Vpk = 16.5V Vav = 13.25V / so power = 13.25V × 4.22A = 56W scope maths = 55W / From waveform 11 duration ≈ 60ms so energy = 3.36J
Mosfet Safe Operating Area (SOA) & Thermal considerations
Mosfet SOA / Using IRLB3034 as an example of an SOA chart, because used it in the thermal calculation example below	At 11.5V supply the current pulses are about 15A with a triangular shape of width 23µs, but to allow a generous safety margin use 30A & 50µs. SOA data usually has plots of curves at 100µs so use this instead of 50µs giving an even greater safety margin. The voltage for the SOA will be 15V. / Taking the IRLB3034 SOA as an example its DC SOA at 15V is only about 3A, but its 100µs SOA is about 200A, however this is for a temperature rise of 150°C from 25°C to 175°C. For a good lifetime better to restrict the temperature rise to 75°C so therefore the 100µs SOA current would be reduced to 100A. / This is still in excess of our requirement of 30A so is OK. / The actual temperature rise for the 15A 23µs triangular pulse will be very considerably lower than 75°C.
Thermal calculations / just to get an estimate of whether a heatsink is required or not.	thermal energy formula: Q = m × c × Δt / Q = energy J / m = mass kg / c = specific heat capacity J / kg · K / Δt = temperature rise K (or °C) / If the energy was dumped in an aluminium heatsink / specific heat capacity = 900 J / kg · K / allow 20K temperature rise for the aluminium / ∴ mass = 0.19g / If the energy was dumped in a copper sheet / specific heat capacity = 385 J / kg · K / allow 20K temperature rise for the copper sheet / ∴ mass = 0.44g / For reference the total mass of a TO-220 is about 1.9g, so it may be able to absorb the energy without an additional heatsink.
Thermal simulation model / Using IRLB3034 in a TO-220 package as an example. Because it has a thermal model on the data-sheet. (Although it only has a moderate DC SOA its pulse SOA is acceptable). / Triangular power pulses applied with 55W average, see waveform 13. / R5 with a thermal resistance of 62K/W represents a TO-220 without a heatsink. / In the model: / current represents thermal power / voltage represents temperature	IRLB3034 thermal model results / Red = junction temperature rise at 60ms, average = 50°C / & temperature ripple due to the individual triangular power pulse is small at about 2°C. / green = TO-220 case temperature rise, at 60ms = 35°C / So a TO-220 package without a heatsink has an acceptable temperature rise for a single 60ms burst of pulses, even with an 11.5V supply.