Remora1 Production Test
Revision 0.0
December 2023

Pad identification

VCC, 12V4
VDD, 3V3
GND
SWD_IO
SWD_CLK
PB6
VBUS (VIN)
PA2
PA15
GND

VDC,10.3V

Procedure
setup / action	measure	expected result
visual inspection	check for no missing or misplaced parts, no bad joints or solder bridges	all OK
Low Voltage Start & Run
set power supply to 1.5V, but output off
connect power supply to + & - terminals
turn power supply output on	power supply current	162mA to 212mA
	VCC to GND	11.954V to 12.914V
	VDD to GND	3.234V to 3.366V
reduce power supply voltage to 1.2V	power supply current	224 mA to 232mA
	VCC to GND	9V to 11.3V
High Voltage Test
increase power supply voltage to 13.5V	power supply current	33mA to 37mA
	VDC to GND	8.7V to 12.7V
	VCC to GND	11.954V to 12.914V
Memory Programming
programme the flash memory
reduce power supply voltage to zero & turn off
Operation With Motor Connected
connect motor, make sure its mechanically secure
turn power supply on
slowly increase power supply voltage	check motor rotation	normal rotation
reduce power supply voltage to zero & turn off
Reverse Polarity Test
reverse connections to + & - terminals
turn power supply on, increase power supply voltage to 13.5V	power supply current	<1.7mA
reduce power supply voltage to zero & turn off
restore normal connections to + & - terminals
turn power supply on, increase power supply voltage to 13V	check for motor rotation	normal rotation
End of Tests
reduce power supply voltage to zero & turn off
end

Revision History
revision	date	changes
0.0	29 December 2023	initial draft, based on 2 prototypes with adaptor board